## Slide 1
Introduction to the linear system analyzer app
03

## Slide 2
The Linear System Analyzer app lets you analyze time and frequency responses of LTI systems.
Description to the Linear System Analyzer App

## Slide 3
01
02
03
04
Inspect key response characteristics, such as rise time, maximum overshoot, and stability margins.
View and compare the response plots of SISO and MIMO systems, or of several linear models at the same time.
Generate time response plots such as step, impulse, and time response to arbitrary inputs.
Generate frequency response plots such as Bode, Nyquist, Nichols, singular-value, and pole-zero plots.
Fuction of the Linear System Analyzer App

## Slide 4
The method of open the app
1. On the Apps tab, under Control System Design and Analysis, click the app icon.
2.MATLAB command prompt: Enter ltiview

## Slide 5
Related Examples
1.Build a transfer function model
2.Import H to the linear system analysis

## Slide 6
Related Examples
From this step response,you can set characteristics to get peak response、setting time 、rise time and stead state.

## Slide 7
Related Examples
3.You can add more plots to the Linear System Analyzer:
Select Edit > Plot Configurations.
In the Plot Configurations dialog box, select the number of plots to open.

## Slide 8
Related Examples
From those pictures.we can get Nichols chart、bode diagram 、pole-zoro map and the like.based on this ,we can judged the stability of the system.